## Slide 1
Chapter 10 Forced-Convection External Flows
This chapter is the first to describe convection – one of the 3 modes of heat transfer.
It is the most difficult
chapter for readers to
learn and for instructors
to teach.
Why?

## Slide 2
Reasons of Difficulty
If we spend too much time, there will not be enough time left for other topics.
If we do not spend
enough time, we will
not be able to cover
this topic completely.

## Slide 3
Nonlinearity
Conduction is basically a linear phenomenon.
Convection is basically a
nonlinear phenomenon.
The fluid carries enthalpy:
for example, (T)
uT is a nonlinear term, because
both u and T are unknowns.

## Slide 4
Pressure and Continuity Equation
In addition to the nonlinearity, we also have to solve the pressure field.
x-direction momentum Eq. for u
y-direction momentum Eq. for v
energy equation for T
p = ρRT for ρ
Which equation will govern p?
answer: continuity equation
But p does not exist in C eq.

## Slide 5
An Official Procedure to Solve 2-D Steady State Convection Problems
Solve for u, v, T, p, and ρ
Obtain T(x, y)
Obtain (∂T/∂y)y=0
Obtain qs = - k(∂T/∂y)y=0
The story ends here.

## Slide 6
Where Is the Heat Transfer Coefficient?
Where is h?
What happened to h?
How does h play a role
in the problem?
Do we need h?

## Slide 7
Let us pay attention.
Attention!
Attention!
Many heat transfer scholars
have misinterpreted this
concept.
Important Concept

## Slide 8
h Is Merely for Convenience
Usually, we are interested in finding qs.
Sometimes, we walk extra miles to find h by computing h from h = /( – ), so
that other users can conveniently find q’’s
from = h( – ) .
Nu is simply a
dimensionless h,
defined as Nu = hL/k
or = hx/k.

## Slide 9
10-minute Classroom Interactive Question
Consider an enclosure as shown (L >> H). Assume that air inside is perfectly quiescent. Find Nu (=hH/k) at the bottom face.

## Slide 10
q’’s = k *(0-100)/0.1m
= - 1000 W/.
So, h = q’’s / (0 – 100)
= k*10 W/-K.
Then, Nu = hH/k = 1.
MATLAB code
clc; clear;
H=0.1; k=1; % k value is irrelevant.
dT=0-100; qs = k*dT/H;
h = qs/dT; Nu=h*H/k % = 1
Answer:
Nu = 1 is a trivial answer, but it serves as the minimum.

## Slide 11
Other Topics
Soup Blowing
Cubic Velocity Profile
Finding can be readily
followed by reading the
textbook.

## Slide 12
Chapter 11 Forced-Convection External Flows (II)
Outline
Nondimensionalization
(Ndm)
Important Physical
Parameters
Categorization of Heat Convection
Derivation of Governing Equations

## Slide 13
Nondimensionalization (Ndm)
Δu/Δx (dimensional)
define u* = u/; x* = x/L;
u* is dimensionless;
is a reference velocity;
Hence, Δu/Δx = (/L)(Δu*/Δx*)

## Slide 14
Ndm May Identify Parameters
For example, a governing equation
ui (-uw + ui)/Δx = 𝜈 (uw – 2ui + ue)/
can be transformed into: (Re) ui*(-uw* + ui*)∆x* = uw* - 2ui* + ue*,
where
Re = L/𝜈 .

## Slide 15
Ndm (cont’d)
A boundary condition
- k dT/dx = h (T – ) can be
transformed into
- d𝜃/dx* = Bi 𝜃, where
𝜃 = (T – )/ΔT, and Bi = hL/k.

## Slide 16
Incidentally
Bi = hL/
(Biot number)
Nu = hL/
(Nusselt number)
“s” stands for solid;
“f” stands for fluid;

## Slide 17
An engineering problem
sometimes can be very
involved.
It could involve engineers,
applied mathematicians,
programmers, among others.
They need to communicate.
Yet they may speak different
languages.
Task Sharing

## Slide 18
The unified language for all the scientists and engineers is pure numbers that are dimensionless without any physical meanings attached.
3 + 5 = 8
not 3 J/K-s + 5 J/K-s = 8 J/K-s
Unified Language

## Slide 19: 10-minute Classroom Interactive Question
Ndm the following governing equation:
ρ cp u dT/dx = μ (du/dy.

## Slide 20
Let u* = u/, 𝜃 = (T- )/∆T
After straightforward algebra,
we obtain
Re u* d𝜃/dx* = Ec (du*/dy*,
where Ec (Eckert number) = /(cp ∆T)
Answer:

## Slide 21
Categorization
Forced Convection and Free Convection
External Flows and Internal Flows
Laminar Flows and Turbulent Flows
Incompressible Flows and Compressible
Flows
Others

## Slide 22
Chapter 12 Forced-Convection External Flows (III)
Outline
The official procedure
to find Nu = 0.664
is beyond the scope of this course.
Let us learn a quick and approximate
way.

## Slide 23
The Official Procedure
Solve u(x,y), v(x,y), p(x,y), T(x,y), and
ρ(x, y) simultaneously.
Watch out the direction of on the top face.

## Slide 24
Nu Correlation
(a) For given values of Re and Pr, find T(x, y)  ∂T/∂y at the wall  q’’s  h  Nu
(b) Vary values of Re and Pr,
and repeat (a).
(c) Curve-fit the data into
a correlation.

## Slide 25
Beyond the Scope
This official procedure is beyond the scope even for a graduate course.

## Slide 26
A quick and approximate
procedure is to decouple
u, v, p, and ρ from T.
Simply solve
[- + T(j)]/HCL = α [(T(j-1) – 2T(j) + T(j+1)],
where HCL stands for Heat Convection Length.
Nu Correlation (continued)

## Slide 27
Always Remember T(2)
T(2) is the most interesting quantity to us.
Not T(3), T(4), … T(1000).
If you remember this piece
of information, you are
ahead of many of your peers.
why? Why?

## Slide 28
T(2)  q’’s = k (Ts – T(2))/Δy
 h = q’’s / (Ts – )
 Nu = hL / k.
That is why T(2) is
most important and
interesting to us.
T(2) yields q’’s

## Slide 29: 10-minute Classroom Interactive Question
Consider an air flow over a flat plate.
Re = 1e4; Pr = 0.72; k=0.026;
x = 0.1m; Ts = 20C; T∞=100C;
T(2) has been computed to
be 20.4761C at ∆y=1e-5m.
2
Find local x=0 x=0.1

## Slide 30
Answer:
q’’s = k (Ts – T2)/Δy = - 1237.9 W/
h = q’’s/(Ts – ) = 15.4734 W/-K
Nu = hx/k = 59.513;
Let us compare with:
clc; clear
Re=1e4; Pr=0.72;
Nu=0.332*Re^0.5*Pr^(1/3)
% = 0.59.513
Shall we compare the black swans with ducks?

## Slide 31
dT/dy at wall, q’’s, h, and Nu
These 4 quantities are like siblings. If we know one of them, we can readily find the other three.