## Slide 1
Published by Cognella, Inc. (©2012)
Tien-Mo Shih
The University of Maryland
College Park, Maryland, USA
“The Ultimate Purpose of Education is to Promote Peace and Enrich Life.”

## Slide 2
Table of Contents
There are 7 parts in the textbook.
There are approximately 3 lessons
in each part
Part I: Fundamentals in Heat Transfer
Part II: Slightly Advanced Conduction
Part III: Transient Heat Conduction
Part IV: External Heat Convection
Part V: Internal Heat Convection
Part VI: Free Convection, Turbulent
Convection, Heat Exchangers
Part VII: Radiation

## Slide 3
Chapter 1 Introduction of Heat Transfer (I)
Outline
Need a Second Check
A Simple Coke Problem
Uniqueness of the Course
Heat Transfer Examples in Daily Life
Structure of the Book

## Slide 4
Thermodynamics vs. Heat Transfer
Thermodynamics = First Income of a Household
Heat Transfer = Second Income of a Household
Only First Income is no longer enough.
They also look like twins.

## Slide 5
A Simple Coke Problem
How long does it take for a can of Coke, taken out from the refrigerator at 5C, to
warm up to 15C in a room at 25C?
First Law of Thermodynamics dictates: ΔU = , where
ΔU = m cv (T – Tp)/Δt,
There are 2 unknowns: Q_in and T.
But there is only one equation!!

## Slide 6
Need Another Equation
We are unable to solve the previous Coke problem. Unless we have one
more equation. = function of T

## Slide 7
A 10-minute Classroom Interactive Question
A can of Coke is taken out from the refrigerator at 5C, and is placed on a table in a room at 25C. Sketch T(t). Related questions: (1) What do you base on to sketch the curve like that?
(2) Are you able to compute T(t) now? If not, why not?

## Slide 8
Answer:
T with increase with t exponentially. Initially, Coke is cold, so T_coke will increase rapidly. As it is warmed up, the warming process will slow down.
(2) No, we are not able to compute T(t) now. Because we have not learned how to related Q_in with T. (We did learn: ∆U = m ΔT from thermodynamics) (Lesson 6 will present this problem)
clc; clear;
c1=0.7; t=linspace(0, 5, 51);
T=(-20)*exp(-c1*t)+25;
plot(t, T)
A MATLAB code to plot T vs. t

## Slide 9
Uniqueness of the Course
Simple MATLAB codes
Many daily-life problems
2 or 3 grid nodes
Emphasis on fundamentals and simplicity

## Slide 10
Heat Transfer Examples in Daily Life
Getting up from bed -- chilly
Open the curtain – radiation loss/gain
Layer of ice forming on the windshield
Airplane flying, car moving – combustion
Drink a cup of coffee
Happy Birthday Party – candle burning Frying yummy potato patties
There is a will; there is a way.
There is there is heat transfer

## Slide 11
Structure of the Book
7 Parts (3 lessons for each part)
Part 1: Introduction, 1-D steady state conduction
Part 2: slightly advanced steady state conduction
Part 3: transient heat conduction
Part 4: external convection
Part 5: internal convection
Part 6: free convection, turbulent flows, heat exchangers
Part 7: radiation

## Slide 12
Chapter 2 Introduction of Heat Transfer (II)
Outline
Fourier Law for Conduction
Law of Convection, q’’ = h(Ts - T∞)
Stefan-Boltzmann Law
Wind-Chill Factors
Ice Layers Forming on Car Windshields
ADW (Assume, Draw, Write)

## Slide 13
Fourier Law of Conduction
q’’ = - k ∂T/∂x (in W/)
(called heat flux)
Why is there a negative sign? q = q’’ A (in W) (called “heat flow rate”)
“prime” means “per meter”
Hot Cold

## Slide 14
Law of Heat Convection
q1 = h A ( – T1)
or
q2 = h A (T2 – ).
Which one should we use?
See ADW in slide 7

## Slide 15
Wind-Chill Factors (WCF)
h_windy (37 – )
= h_calm (37 – WCF)
WCF is a fictitious temperature.

## Slide 16
A 10-minute Classroom Interactive Question
On a Sunday, you and your family go for an outing. In the morning, T_air = 25C, and h = 20 W/-K. At noontime, it becomes windy with h = 40 W/-K. At the same time, you nonetheless feel the same cooling effect. What is T_air at noontime?

## Slide 17
Answer:
q’’ = 20 *(37C – 25C) = 240 W/.
240 = 40* ( 37C – x )  x = 31C.
MATLAB code: clc; clear
h1=20; Tair1=25; h2=40;
qs=h1*(37-Tair1);
Tair2= 37-qs/h2 % = 31C

## Slide 18
Stefan-Boltzmann Law of Radiation
q_rad = A εσ (Watts)
For Blackbodies,
ε = 1

## Slide 19
Ice Layers Forming on Car Windshields
q_supply =
q_rad + q_conv
Assume
q_supply ≈ 0
εσ + h (T – T∞) = 0
Nonlinear Equation!

## Slide 20
Assume, Draw, and Write (ADW)
Assume: hot system, cold ambience
Draw: the arrow
Write: the governing equation
∆U = - h A Δt ( – ) …. Eq. (1)
Assume: cold system, hot ambience Draw: the arrow Write: the governing equation ∆U = h A Δt (– ) …. Eq. (2)
Equations (1) and (2) are the same, as long as we follow the rule of ADW.

## Slide 21
Chapter 3 One-D Steady State Heat Conduction
Outline
Governing Equation
Single Slab
Multiple Slabs
Overall Resistance
Boundary Conditions

## Slide 22
Governing Equations
∆U = – .
Steady State  ΔU = 0.
Also, = kA[T(i-1) – T(i)]/∆x,
= kA[T(i) – T(i+1)]/Δx.
So, T(i-1) – 2T(i) + T(i+1) = 0.

## Slide 23
Single-Slab Problems
Based on the governing equation in the previous
slide, to find interior nodal T’s is a trivial task.
We will focus on finding T’s on the two faces, at x = 0 and x = L
There are 8 possible combinations of boundary conditions, excluding both q1 and q2 are given.

## Slide 24
A 10-minute Classroom Interactive Question
If the temperature of our body tissue is 37C, T_room is 25C, and the thickness of the tissue is 0.002m, find T_skin. Relevant data: L = 0.002m,
h = 20 W/-K,
k = 0.61 W/m-K

## Slide 25
Answer:
k_skin*(37 – T_skin)/L = h (T_skin – T_room)
or T_skin = (37 + Bi*T_room)/(1 + Bi), where Bi (Biot number) = h L / k_skin.

## Slide 26
Numerical Experiments
clc; clear
k=0.61; h=20; L=0.002;
Bi = h*L/k % = 0.0656
Troom = 25;
Tskin = (37 + Bi*Troom)/(1+Bi) % =36.262C
What if:
h increases, L increases, or k increases?

## Slide 27
Multiple-Slab Problems
q = h1*(Tinf1 – T1)
= ka*(T1 – T2)/La
= kb*(T2 – T3)/Lb
= h2*(T3 – Tinf2) Why? Because (1) 1-D, (2) steady state,
(3) q_gen = 0.

## Slide 28
Rearrange: q /h1 = Tinf1 – T1
q*La/ka = T1 – T2
q*Lb/kb = T2 – T3
q/h2 = T3 – Tinf2
q*(1/h1 + La/ka + Lb/kb + 1/h2) = –
Multiple-Slab Problems (cont’d)
cancel
cancel

## Slide 29
Overall Resistance
R = 1/h1 + La/ka + Lb/kb + 1/h2