## Slide 1
Chapter 7 Transient Lumped-Capacitance Heat Conduction
Outline
Why Studying This Model?
ΔU is the Key Term
Explicit Method vs. Implicit Method
Biot Number, Bi
Why Stirring the Food?
The only attribute that is not transitory on earth is “transitory” itself.

## Slide 2
Why Studying This Model?
Desire to obtain a quick and
true approximation. (case a)
Desire to obtain a quick
approximation. However,
the accuracy of the solution
is not essential to us. (case b)

## Slide 3
Explicit Method and Implicit Method
Consider a small copper plate
placed in the outer space.
m cv (T – Tp) = εσ (1)
( explicit )
m cv (T – Tp) = εσ (2)
( implicit )
Solving Eq. (1) is easier.
Solving Eq. (2) is more stable.
Tp: temperature at the previous time step
T : temperature at the current time step.

## Slide 4
Biot Number, Bi
definition: Bi = h L /k
h=100 W/-K,
k= 1 W/m-K, L = 0.1m
Bi = 10 (LC model Invalid)
h = 1 W/-K, k= 100 W/m-K, L = 0.1m Bi = 0.001 (LC model valid)

## Slide 5
A 10-minute Classroom Interactive Question
Take a can of Coke out from the refrigerator. After 2∆t, find T_coke. Relevant data include:
m=0.28 kg, cv=4180 J/kg-K, h=4.8 W/-K, A=0.01 , =25C, T_init = 5C, Δt=200s.
Use the simple explicit method.

## Slide 6
Answer:
clc; clear
m=.28; cv=4180; h=4.8;
A=0.01;
Tinf=25; Tp=5; dt=200;
c1=h*A*dt/(m*cv);
T=Tp + c1*(Tinf-Tp) % 5.164C
Tp = T; % remember to update Tp
T=Tp + c1*(Tinf-Tp) % 5.3267C

## Slide 7
Why Stirring the Food?

## Slide 8
Governing Equations for T1 and T2
m cv (T1 – T1p)/∆t = A – A k (T1 – T2)/∆x,
m cv (T2 – T2p)/Δt = A k (T1 – T2)/Δx.
with stirring: T1 = 37.4C and T2 = 34.5C
(more uniform)
without stirring:
T1 = 46.5C and T2 = 25.4C

## Slide 9
k Does Not Play a Role
In lumped-capacitance systems, k does not
appear.
k has been assumed to be
relatively large, such that
T is uniform inside the
system.

## Slide 10
Chapter 8 One-D Transient Heat Conduction

## Slide 11
Governing Equation for T2
First Law of Thermodynamics dictates:
ΔU = , where
ΔU = m cv (T2 – T2,p)/Δt,
q1 = k Ac (T1 – T2)/Δx,
q2 = k Ac (T2 – T3)/Δx, q3 = h p Δx (T2 – T∞)

## Slide 12
Four Governing Equations
Thus, at t = ∆t, we have
T1 – 100 = 0
-r T1 + (2r + 1 +c2) T2 – r T3 = Tp2 + c2 T∞
-r T2 + (2r + 1 + c2) T3 – 0*T4 = Tp3 + c2 T∞
T3 – T4 = 0,
where r = α Δt / (Δx, c2 = h p Δt / (ρ cv Ac)

## Slide 13
The Solution Procedure
(a) Use T = a \ b’
(b) Update Tp = T
(c) Repeat and march in time
(d) Walk extra miles by checking Global Energy Balance
Same concept for n = 4000 nodes

## Slide 14
Special Cases
Let c2  0 (or h  0) Then the problem is reduced to 1-D transient slabs.
Let t  ∞ Then the problem is reduced to steady state fins.
Let k  ∞ Then (dT/dx  0, what happens to q_base?

## Slide 15: Temperature History of the Fin

## Slide 16: 10-minute Classroom Interactive Question
Consider a copper fin with only
One Interior node as shown.
Relevant data include:
Tb=T1=500K; ε=0.8; σ=5.67e-8;
k=398; ρ=8933; =385;
D=0.006m; L=0.2; nx=2;
Δt=10s; Initially, T2p=500K;
Find T2 after 2∆t
T1 T2 T2
The fin tip is insulated.
(T3 ≈ T2). It is placed in the outer space.

## Slide 17: Answer:
Tb=500; e1=0.8; sig=5.67e-8;
k=398; rho=8933; cv=385;
D=0.006; Ac=D*D*pi/4; p=pi*D;
L=0.2; nx=2; dx=L/nx; dxs=dx*dx;
m=rho*Ac*dx; dt=10; T2p=500;
c1=dt*k*Ac/(m*cv*dx); c2=dt*e1*sig*dx*p/(m*cv);
T2=T2p + c1*(500-T2p)-c2*T2p^4 % = 494.5K
T2p=T2; % update T2p, very important!
T2=T2p + c1*(500-T2p)-c2*T2p^4 % = 489.9K

## Slide 18: Benefits of Using MATLAB Codes
Changing 2 nodes  20 nodes  2000 nodes is
a matter of just changing one single statement.
Students can change values of parameter values and run numerical experiments.
Students can check the
validity of the analysis by
monitoring the global energy
balance conveniently.

## Slide 19
Chapter 9 Two-D Transient Heat Conduction
To save time, instructors may
consider skipping this lesson.
Because there are simply
two more terms in the governing equation: q_south and q_north

## Slide 20
Or, Let Us Consider the 911 Tragic Problem
On 9/11/2001, why did WTC twin towers collapse?

## Slide 21
Facts Related to 9/11 Catastrophe
93rd floor of one of the Twin Towers was hit by the airplane.
The temperature of the
burning jet fuel is ≈ 1000C.
At 700C, the steel column
will lose its strength.
At 1000C, the steel column
will melt.

## Slide 22
Collapsing of Twin World Trade Centers
We can understand that the
upper portion of the building
could fall off.
But why should the entire
building, including the portion
below the 92nd floor, collapse?

## Slide 23
Question: After one hour, Could T_steel Rise to 700C?
A 2-D transient analysis
may help.

## Slide 24
Did Steel Columns Melt?

## Slide 25
According to the 2-D transient computation
(side view), and the 1-D transient computation (longitudinal view), T is lower than 200C one hour after the collision.
See the textbook.
Computational Results

## Slide 26: 10-minute Classroom Interactive Question
Consider a 2-D concrete column.
Initially, the air and the
column are at 20C. Suddenly,
T_west is raised to 1000C.
Relevant data include:
k = 0.8; ρ = 2100; =1100;
Lx=Ly=0.3m; Δt = 100s; one node;
Find T1 at t = 100s. Use the implicit
method.

## Slide 27
clc; clear
rho=2100; k=0.8; cv=1100; aLf=k/(rho*cv);
Lx=0.3; dx=Lx/2; dt=100; dxs=dx*dx;
r=aLf*dt/dxs; %dimensionless aspect ratio parameter
Tp=20;
T=(Tp+ r*(1000+3*20))/(1+4*r)
% = 21.5C
Answer:
At t = 200s, T is likely to be higher than 23C or lower?

## Slide 28
Answer: (cont’d)
The increase in T from T(to T(2 is likely to be slightly less than the increase in T from T(0) to T( In most of the transient conduction problems, the change in T is most drastic initially.
Very much like the passion
at the first sight, decaying
with time…..