## Slide 1
Chapter 13 Forced-Convection Internal Flows (I)
Outline
two flow regimes
simple algebraic equations
for the developing regime
analytical result for the
fully-developed regime
applications

## Slide 2
Two Flow Regimes

## Slide 3
Use Staggered Grid in Developing Regime
A big issue for incompressible
flows
cumbersome but rendering
the coefficient matrix
non-singular
beyond the scope

## Slide 4
Momentum Balance over Computational Cell for u1 and Mass Balance for p1
(p1 – p3)*Δy + μ*(u2-u1)*Δx/∆y
= ρ*u1*(u1-)*Δy.
( – u1)*Δy + (0-v1)*Δx = 0.
http://commons.wikimedia.org/wiki/File:TrumpeterSwan.jpg

## Slide 5
6 u’s + 3 v’s + 6 p’s = 15 unknowns
p7 cell is assumed to be in the
fully developed regime, and is
taken to be a reference pressure.
[A]{q} = {b} can be set up.
Place the nonlinear terms
on the right-hand side
Solve the matrix system
Iterate till converging
Solution Procedure

## Slide 6
Analytical Solution for Fully Developed Regime
u is only a function of y,
not a function of x
No momentum changes
Friction force is balanced
by the pressure drop.

## Slide 7
μ u/d = dp/dx,
u*/d = - B,
where B = - (/μ um)(dp/dx),
u* = u/um , y* = y/b.
At y* = 0 (centerline), du*/dy*=0
At y* = 1 (at the wall), u* = 0
Nondimensionalization (Ndm)

## Slide 8
10-Minute Classroom Interactive Question
What is the minimum
power (Watts) of a blower
that is required to drive a
Laminar fully developed airflow through a duct? Data include:
ρ=1.16 kg/; 𝜈=1.6e-5 /s;
L=70m; b=0.15m; um=20 m/s;
Z=0.5m;

## Slide 9
Answer:
clc; clear
rho=1.16; mu=rho*1.6e-5;
L=70; b=0.15; um=20;
Z=0.5; Ac=2*b*Z;
Q=um*Ac;
dp = L*um*3*mu/(b*b)
power = dp*Q % 10.4 W

## Slide 10
Main Difference between Boundary- Layer Flows and Developing Channel Flows?
In developing channel flows, uc (equivalent to in B-L flows) increases from um to 1.5 um. Hence dp/dx ≠ 0.

## Slide 11
Chapter 14 Forced-Convection Internal Flows (II)
Outline
find an analytical solution
definition of Tm
Why do we need Tm?
justify ∂T/∂x = const.
for the case of q’’s = const.
Note that ∂T/∂x ≠ const.
for the case of Ts = const.

## Slide 12
Analytical Solution Is Possible
It is not easy to find an
analytical solution for
a heat-convection problem.
steady state, v ≈ 0, and
the conduction in the x
direction is negligible.
u ∂T/∂x = α T/∂.

## Slide 13
∂T/∂x = constant
If not, it is difficult to find
T(x, y) analytically.
Conditions for ∂T/∂x = const.
to be true are:
(a) q’’s = const.
(b) 𝜃 = (T- Ts)/(Tm – Ts)
= a function of y only.
Incidentally, (b) is known
to be thermally fully developed.
I want “excitement”, not “constant”!

## Slide 14
Why Is Tm Introduced?
= /b
Be careful. It is NOT:
= /b
enthalpy rate carried by the fluid in the channel
= ()
Do we mean “rate” or “rat”?

## Slide 15
It is a good logical problem.
Let us adopt a procedure,
called, method of genetic chart,
to work on this problem.
Justification of ∂T/∂x=constant

## Slide 16
fact1a: definition of 𝜃
fact1b: q’’s = constant
fact1c: q’’s = - ρ cp b um dTm/dx
These are given conditions.
We shall call them facts of
the first generation
Facts of the 1st Generation

## Slide 17
A Fact of the 2nd Generation (F1a)
If we differentiate 𝜃 with respect to x, i. e.,
𝜃 (Tm – Ts) = T – Ts,
we obtain
(dTm/dx – dTs/dx) 𝜃 = dT/dx – dTs/dx
or we can write
F1a  F2a

## Slide 18
If we differentiate 𝜃
with respect to 𝜉 (=y/b),
we obtain
( – Ts) d𝜃/d𝜉 = b ∂T/∂y
or we can write
F1a  F2b
A Fact of the 2nd Generation (F2b)
Hmm, Zekey or Donbra?

## Slide 19
A Fact of the 2nd Generation (F2c)
Because 𝜃 is a function of 𝜉 only,
we obtain
(d𝜃/d𝜉)𝜉=1 is a pure number.
( 𝜉=1 is at the wall, or y=b)
- 2.0586
such as:

## Slide 20
Facts of 3rd, 4th, and 5th Generations
3rd generation: Tm – Ts must be a constant.
4th generation:
∂T/∂x = dTs/dx = dTm/dx
5th generation:
∂T/∂x = constant.

## Slide 21
A Genetic Chart
F1a F2a
F1b F2b F3 F4 F5
F1c F2c

## Slide 22
10-Minute Classroom Interactive Question
Consider two fluid chunks: fluid chunk 1: u1 = 5 m/s, T1 = 20C;
fluid chunk 2: u2 = 3 m/s, T2 = 40C;
What is the value of Tm?
u1 = 5 m/s, T1 = 20C
u2 = 3 m/s, T2 = 40C

## Slide 23
Answer:
clc; clear
n = 2;
u1=5; T1=20; u2=3; T2=40;
um = (u1+u2)/2;
Tm = (u1*T1 + u2*T2)/(n*um)
% = 27.5C
% NOT 30C

## Slide 24
Chapter 15 Forced-Convection Internal Flows (III)
Outline
An Analytical Procedure
to Find Nu
Dimensionless Governing
Equation
Logical Steps: 𝜃  recover T
 find (∂T/∂y  q’’s  h  Nu
Applications

## Slide 25
Dimensionless Governing Equation
G ( – 1) = 𝜃/d,
where G = - 1.5(um b/α)(b/∆T)(dT/dx) = constant,
𝜉 = y/b,
ΔT = Tm – Ts.
How did we find the equation
above? Practice, practice, and practice.

## Slide 26
The Solution of 𝜃 Profile
After algebra, we obtain
𝜃 = 3.0878(/12 - /2 + 5/12).
At 𝜉=1, 𝜃=0 as expected.
Also, 𝜃m = 1 by definition.

## Slide 27
Find Nu
Logical Steps:
start with 𝜃  recover T
 find (∂T/∂y  q’’s
 h  Nu.
Sometimes finding 𝜃 is
a job belonging to
applied mathematicians
or programmers.

## Slide 28
Detailed Procedure of Finding Nu
(a) T = Ts + 𝜃ΔT, where
∆T = Tm – Ts,
(b) ∂T/∂y = (d𝜃/d𝜉)∆T/b,
(c) (∂T/∂y)y=b = (d𝜃/d𝜉)𝜉=1∆T/b,
(d) (∂T/∂y)y=b = - 2.0586∆T/b,
(e) q’’s = - k (∂T/∂y)y=b ,
(f) h = q’’s/ΔT = 2.0586k/b,
(g) Nu = hb/k = 2.0586.

## Slide 29
The detailed procedure in
the previous slide is a
job for engineers.
Without nondimensionalization (Ndm), the procedure of finding
T(x,y) directly is quite cumbersome.
one more evidence of the
advantage of using Ndm
Post-Processing

## Slide 30
We have two independent
equations:
Nu = 2.0586
(for the case of q’’s = const)
(b) q’’s = - (ρ cp b um) dTm/dx
Applications

## Slide 31
10-Minute Classroom Interactive Question
Consider a thermally fully developed water flow. Relevant data include:
b = 0.01m; L=5m, Z=1m;
k = 0.61; ρ=1000; cp=4180;
𝜈 = 9.5e-7 /s; um = 0.04m/s;
Tm_in =20C; Ts_in = 90C;
Find q’’s and Ts_exit

## Slide 32
Answer:
clc; clear
% heating of the water flow and qs=constant
b=0.01; Lx=5; Z=1; % geometry of the channel
k=0.61; rho=1000; cp=4180; aLf=k/(rho*cp);nu=9.5e-7;%fluid properties
um=0.04; Tm_in=20; Ts_in=90; % flow conditions
pr=nu/aLf; re=um*b/nu; %=421.05
Pe=pr*re; Nu=2.0586;
% calculation of the problem
Qs = Nu*k*Lx*Z*(Tm_in - Ts_in)/b % = -43.95 kW
mflow = rho*b*Z*um;
Tm_ex= Tm_in - Qs/(mflow*cp)% =46.2865C
Ts_ex= Tm_ex + Ts_in - Tm_in % = 116.2865C

## Slide 33
Comments
We have two independent
equations. Therefore, we
can only afford to have two
unknowns.
In principle, two variables
among b, L, um, Tm_in,
Tm_exit, Ts_in, and Ts_exit
can all be unknowns.